## Slide 1
Port_Init
- Set port to SCL/SDA function
I2C_Initial
- Peri. Clock Enable / I2C Block Reset / I2C Enable / I2C Interrupt Enable
I2C Ack Enable / Set Slave Own Address / I2C Speed / I2C Data Hold Time
Master Transfer Function
- Set write/read buffer & write/read count
I2C_Initial
I2C_Start
Timeout Check
I2C->ST
&BUSY
No
Yes
I2C_Initial
I2C Interrupt Handler
I2C->ST
&MLOST
&STOP
I2C->ST
&RXACK
STOP Generate
I2C_Initial
No
No
Yes
I2C->ST
&TMOD
Yes
write
count?
read
count?
No
Yes
I2C->DR = txBuffer
read
count?
Yes
No
Restart Generate
Yes
STOP Generate
No
rxBuffer = I2C->DR
STOP Generate
NoAck Generate
No
Yes
if(readcount==1)

## Slide 2
Port_Init
- Set port to SCL/SDA function
I2C_Initial
- Peri. Clock Enable / I2C Block Reset / I2C Enable / I2C Interrupt Enable
I2C Ack Enable / Set Slave Own Address / I2C Speed / I2C Data Hold Time
Slave Set Function
- Set write/read buffer
Timeout Check
I2C_Initial
I2C Interrupt Handler
I2C->ST
&MLOST
&STOP
I2C_Initial
No
Yes
No
Yes
I2C->ST
&GCALL
I2C->DR = txBuffer
rxBuffer = I2C->DR
I2C->ST
&TMOD
GCALL Function
(User specific)
No
Yes

## Slide 3
void USI_I2C_Initial(uint8_t ch, uint32_t speed, uint8_t addr, uint8_t ack)
I2C channel number
I2C speed
I2C slave own address
I2C ack enable/disable
void USI_I2C_MasterTransferData(uint8_t ch, uint8_t dev_addr, uint8_t *write_data, uint8_t write_len, uint8_t *read_data, uint8_t read_len)
I2C channel number
slave device address
write data buffer
write data length
read data buffer
read data length
void USI_I2C_SetSlaveData(uint8_t ch)
I2C channel number
#define I2C_DEVICE_ADDRESS 0xA0
#define I2C_SLAVE_OWN_ADDR 0xA0
#define I2C_SPEED 10000
#define I2C_MAX_BUFFER_SIZE 20
#define I2C_MAX_CHANNEL 2
#define I2C_CH0 0
#define I2C_CH1 1
#define I2C_ACK_DISABLE 0
#define I2C_ACK_ENABLE 1
#define I2C_WRITE_MODE 0
#define I2C_READ_MODE 1
#define I2C_IDLE 0
#define I2C_BUSY 1
#define I2C_FALSE 0
#define I2C_TRUE 1

## Slide 4
void USI_I2C_SetSlaveData(uint8_t ch)
{
……
receiveNum[ch] = 0;
transmitNum[ch] = 0;
……
for(i=0; i<I2C_MAX_BUFFER_SIZE; i++)
{
transmitBuffer0[i] = (0x00 + i);
receiveBuffer0[i] = 0x00;
}
……
}
I2C channel number
Set Transmit Buffer
0x00 , 0x01, 0x02, …
(User specific)

## Slide 5
enum i2c_control_flags{ // I2C Control Register Flags
fI2CnEN = (1<<7),
fTXDLYENBn = (1<<6),
fI2CnIEN = (1<<5),
fI2CnIFLAG = (1<<4),
fACKnEN = (1<<3),
fIMASTERn = (1<<2),
fSTOPCn = (1<<1),
fSTARTCn = (1<<0),
};
enum i2c_status_flags{ // I2C Status Register Flags
fGCALL = (1<<7),
fTEND = (1<<6),
fSTOPD = (1<<5),
fSSEL = (1<<4),
fMLOST = (1<<3),
fBUSY = (1<<2),
fTMODE = (1<<1),
fRXACK = (1<<0),
};

## Slide 6
int main( void )
{
unsigned char i;
unsigned char u8TxDat[8];
unsigned char u8RxDat[8];
Init_Port();
Init_Clock();
#if 1 /* Master mode */
USI_I2C_Initial(I2C_CH0, I2C_SPEED, I2C_SLAVE_OWN_ADDR, I2C_ACK_ENABLE);
for(i=0;i<8;i++)
{
u8TxDat[i] = (i + 0x00);
u8RxDat[i] = 0x00;
}
while(1)
{
USI_I2C_MasterTransferData(I2C_CH0, I2C_DEVICE_ADDRESS, u8TxDat, 8, u8RxDat, 0);
}
#else /* Slave mode */
USI_I2C_Initial(I2C_CH1, I2C_SPEED, I2C_SLAVE_OWN_ADDR, I2C_ACK_ENABLE);
while(1)
{
USI_I2C_SetSlaveData(I2C_CH1);
}
#endif
return 0;
}